## Slide 1
Customer Escaped Defect Analysis Report (CEDAR)
Communicating the Results of an 5 whys RCA/EDA to the Customer

## Slide 2: # 2 SW & HW Product Issues – TDD
Issue Description | Relevant Prontos | Key Improvement Actions
Mobily KSA: High frequency of TL17A SW & HW defects, most impactful were: RP3 alarms (multiple root causes) Sleeping cells | Sleeping cells CAS-163519-P3K1/CAS-162042-X5M9 CAS-122724-H4Q5 CAS-155796-K5C3 CAS-95365-Q9L7 | .
 | RP3 alarms CAS-134158-M6S2/CAS-147834-B9P2 CAS-136404-D3M1 | 
MTN Iran: High frequency of TL16SPRE faults, all reappearing in TL18 RE release: Sleeping cells SW Fallback GPS 24hr holdover not functioning IOT (Interference over thermal noise) | Sleeping cells CAS-123832-J3V9 CAS-162042-X5M9 | 
 | SW Fallback CAS-166471-Q9M7 | 
 | GPS 24hr holdover not functioning CAS-165857-H4K9 | 
 | IOT (Interference over thermal noise) CAS-107090-V9C1 CAS-180942-R1S2 | 

## Slide 3
Description:
In Mobily East Region, Nokia is swapping fALU (2G/3G/FDD/TDD) Network to New Nokia Network SBTS SRAN17A , while TDD with TL17 MP5. There are several sites happened the sleeping cell issue and the MSG3=0 , huge MSG1
[TL18SPRE NPI Iran pilot][TL18SPRE]Sleeping cell again in MTN-Irancell.
Cause:
It’s doubted that the issue was caused by unstable DFE flash contents in V2.2A and clear_it feature that degraded the performance, but the root cause is unknown because DFE flash contents and clear_it feature were both developed by 3rd party. And there is no direct evidence from technical aspect showing that this issue related to RF, no alarm to RF module, but after new version updated, the issue fixed.
Escape Reason:
N/A since technical root cause and trigger scenario unknown, but LTE SISO team is progressing two prevent actions related with sleeping cell.
Corrective Action:
The correction was delivered per Nokia internal LTE test result before the customer issue was reported. In LTE test result, some warnings were found in link status monitor without any alarm reported after updating the DFE flash contents from V2.3 to V2.2A with the clear_it dfe operation added. So we rolled back DFE flash contents to V2.3 instead of V2.2A, and removed the clear_it feature.
Preventive / Continuous Improvements:
Adding call on IoT in automatic regression on real HW, LE: 2019/04.
Removal and insert optical fiber repeatedly can be consider as a robustness case, LE: 2019/03.
CO Quality: | <to be added by CT> | Program : | MN Smart Radio SW | Date: Update: | Jan 16, 2019 <Month Yr as needed>
CAS-163519-P3K1 / CAS-162042-X5M9: sleeping cell observed in TL18 P8
Customer
Corporate Logo
Notes: 3

## Slide 4: CAS-122724-H4Q5: RACH degradation after availability fluctuation
Description:
After an update of TDD stations, there is an increase of M8001C6 ((The number of RACH setup attempts for contention based) counter rate from time to time. 99% of RACH requests are unsuccessful.
<Case Opened Date:.> 8th May 2018
Cause:
Rach handles, a pointer to maintain status of preambles in intra-MAC PS, didn't reset during cell reconfiguration, then there was no free one so that preambles were not handled. In the end, Rach setup was failed and M8001C6 was sharp increase.
This is a legacy defect injected from the beginning of LTE release(RL25.)
Escaped Defect Reason:
This is a extraordinary scenario and no SCT cases that cover Rach handles’ memory initializer during cell reconfiguration
Corrective Action:
1, Correction has been delivered from TL17A 3.0 and later releases.
2, Add a SCT case to cover the fault and add it into the CI to prevent the same defect happen again.
Preventive / Continuous Improvements:
1, Technical lesson learned has been shared with relevant Dev team by regular Pronto sharing meeting whose purpose is to continuously develop
the Dev engineer’s competence.
2, Lesson learned from test team, make abnormal testing scenario and analysis conducted together, has been shared within system test
team and current test team has started to perform exploratory test and negative test.
Customer
Corporate Logo
Notes: 4

## Slide 5
Description:
In Mobily East Region, Nokia is swapping fALU (2G/3G/FDD/TDD) Network to New Nokia Network SBTS SRAN17A , while TDD with TL17A 4.0.1. Around 62 sites swapped till date in different Cluster, while around 37 sites are showing overall degradation & counts keeps increasing every next day. Mainly due to High UL/DL BLER.
Cause:
MAC PS sends PDSCH request with 0 PRB and DLPHY doesn’t check this parameter and its consequence cause TX descriptor resource leakage in the subsequent BCP handling. In the end, all TX descriptor resources are gone and hence PDSCH handling malfunctions and as a result normal UE schedule is dead.
Escape Reason:
SCT case does not cover this legacy scenario that MAC PS might schedule 0 PRB PDSCH request. Then this abnormal scenario is slipped away under our eyes.
Corrective Action:
The correction is very simple and straight forward. We just check “numMuPrbs” parameter and drop them whose value is 0 and meaningless for UE schedule. A new SCT case is designed to cover this abnormal scenario and added in the CI as well.
Preventive / Continuous Improvements:
Check all the parameters for the messages sent from MACPS, if some illegal parameter is found, then report error. State: Done.
Sleeping cell feature cluster created(the first Sleeping cell feature LTE3796 implemented in LTE18A).
Abnormal test scenario to detect resource hanging situation was added in the Performance Testing.
Define Customer KPI check list for sleeping cell detection and utilize KPI monitoring platform to detect sleeping cell.
CO Quality: | <to be added by CT> | Program : | MN Smart Radio SW | Date: Update: | Jan 16, 2019 <Month Yr as needed>
CAS-155796-K5C3: BLER and Site stability issues in TDD TL17A 4.0.1
Customer
Corporate Logo
Notes: 5

## Slide 6
Description:
During cell configuration, RUMAG is sending incorrect RP1 Managed object to radio for TDD case, resulting to abnormal timing values in ULPHY. (RP1 Managed object should be 'lteTdd' instead of 'lte’)
Cause:
Human mistake during development. Developer has copy-pasted part of the code and didn’t change.
Code review process was not executed well.
Escape Reason:
Missing System Component Test(SCT) case on development level and insufficient code review.
Corrective Action:
Correction for CAS-95365-Q9L7 is available from TL17A 0.3 and all the later releases.
Preventive / Continuous Improvements:
Lessons learned sharing with the team to highlight severity of simple copy-paste mistake.
Reinforced code review process (at leat done by 1 experienced engineer + mandatory by Technical Leader).
Update of test cases + increased coverage of module tests against similar potential failures.
CO Quality: | <to be added by CT> | Program : | MN Smart Radio SW | Date: Update: | Jan 16, 2019 <Month Yr as needed>
CAS-95365-Q9L7: Zero traffic after TL17A 0.1 SW upgraded
Customer
Corporate Logo
Notes: 6

## Slide 7: CAS-134158-M6S2 : Intermittent RP3 alarms causing degradation in cell availability
Description: Fault 1850 was observed with AHBCC, AHFIC, AHFIA RRHs randomly many days after GA2 activation.
Case Opened Date: 30th of October 2018
Cause:
Memory chips’ operational SW parameters were marginal and not optimized for all memory vendors used in AHBCC/AHFIC/AHFIA products.
This resulted into sub-optimal signal integrity and risk for data corruption on memory bus when corner sample HW was used.
Same platform product defined RFSW (memory parameters) were used for all RF5.1 HW products but HW implementation (e.g. PWB layout and signal routing) of HW variants differed slightly creating the demand of variant specific optimization which was missed.
Escaped Defect Reason:
Second source memory components’ interface testing was not done but platform defined values reused
Memory stress testing was missing in manufacturing plants’ test plans
Corrective Action:
New variant specific parameters for dual band RRHs were introduced in FL18SP 0.1.6 and were ported to parallel active SW branches
Preventive / Continuous Improvements:
Memory bus interface verification was added as mandatory part for second source qualification process (Ongoing)
Manufacturing test plans were updated with memory stress test cases (OK 30th of August 2018)
Lessons learned database was updated highlighting memory bus verification criticality for products that are variants of the lead product (Ongoing)
Notes: 7

## Slide 8: CAS-136404-D3M1 : Failure in optical RP3 interface and cells are down
Description:
<Customer Case Number: Include descriptive content from RESOLVE case.>
<Case Opened Date:.>
Cause:
<Why did it fail? Describe what was wrong in the product. Product viewpoint information.>
<Why was the problem injected? What was the process failure that led to the product failure?>
Escaped Defect Reason:
<Why did it escape the test phases?>
Corrective Action:
<Fault (Pronto) ID>
<SW/HW release info for the correction, or description of other corrective action if not corrected by HW/SW update.>
Preventive / Continuous Improvements:
<What process changes are completed or planned?>
<What test changes are completed or planned?>
<Define how we will confirm that improvement(s) were implemented and being controlled; ie updated process doc, enhanced checklist,
added metric to manage compliance, etc.>
Customer
Corporate Logo
HW case, no response from @Turunen, Timo (Nokia - FI/Oulu) / @Kontas, Veijo (Nokia - FI/Oulu) yet
Notes: 8

## Slide 9: CAS-123832-J3V9 : sleeping cell (MSG1=0) in FlexiMultiradio TD-LTE
Description:
CAS-123832-J3V9 : Fault caused various symptoms. KPI degradation and no paging were the two most visible issues in high level. In this case, there was a sleeping cell situation included.
<Case Opened Date:.> PR reported date: 27.4.2018
Cause:
The function in platform services (PS) clock/time handling area was designed so that performance was not sufficient in all scenarios. Performance was too dependent on the input parameters given to function. Performance degraded when bigger input parameter value was given to function.
Root cause: Clear performance requirements missing in PS clock/time handling area and thus design of the function was left defective from performance p.o.v.
Escaped Defect Reason:
Performance testing of the PS function missing as performance requirements for the function also missing. This level of function performance testing need to be done on component level, can not be on higher testing levels.
Corrective Action:
CAS-123832-J3V9 :
TL16_ENB_0000_001091_000000
The PS function was changed so that performance of the function is not degrading when bigger input parameter value is given to function.
Preventive / Continuous Improvements:
1, Performance requirements for PS clock/time handling area critical functions are under definition.
2, Performance testing of the PS clock/time handling area critical functions will be done when requirements defined.
3, Then performance testing on PS clock/time handling area will be part of the regular component testing and will make sure that functions will fulfill
performance requirements set to those.
Customer
Corporate Logo
Notes: 9

## Slide 10: CAS-166471-Q9M7: [TL18SPRE][FSMFA]DN4369 site SW fallback_(4082)
Description:
CAS-166471-Q9M7 : DN4369 site SW fallback_(4082)
Case Opened Date: 2018-09-25
Cause:
When sysadapt start run and build siteconf unit conf for REAU, will check REAU_L to get stat of REAU, but in this time, there is no RAEU_L, but sysadapt still try read from MoRAEU_L, then triggered null pointer exception, so core dump appear.
Code review process is not rigorous enough, causing code defects that were not discovered at the first time.
Escaped Defect Reason:
UT was missing and code review is not sufficient. This error is triggered only in certain scenarios, ET and ST is difficult to cover subtle issues.
Corrective Action:
Correction for CAS-166471-Q9M7 is available from TL18 3.0 and all the later releases.
Specific correction: Increased null pointer judgement when REAU_l does not exist --> check when REAU_L is null, set unit hwState to "Lost".
Preventive / Continuous Improvements:
1, Code review improvement, adopt some aspects of Fagan inspection methodology to review process.
2, Add UT to cover this corner scenario and added into CI.
3, Adding RAE(not a widely used ALD device type) into system test scope.
Customer
Corporate Logo
Notes: 10

## Slide 11: CAS-165857-H4K9: eNodeB in holdover mode but causing IOT
Description:
CAS-165857-H4K9 : Customer claimed that BTS cannot use 24h holdover when GNSS signal is jammed or spoofed.
<Case Opened Date:.> PR reported date: 18.9.2018
Cause:
The BTS was not prepared for jamming / spoofing (here: the jamming / spoofing causes big phase jump of the PPS generated by GNSS device comparing to world-wide PPS reference) The holdover feature is supposed to be used only when synchronization source become unavailable.
Root cause: The jamming/spoofing robustness has been never promised to customers, hence there was not feature for that. This is requirement missing case from customer side to Nokia. Customer interface problem, not R&D issue.
Escaped Defect Reason:
This scenario was not supposed to be supported. Should be analysed in customer interface why there was requirement missing from R&D – if such support would be needed.
No escape from the R&D pov.
Corrective Action:
CAS-165857-H4K9 :
TL18_ENB_0000_030051_080001
1. The anti-jamming feature in the GNSS device has been launched. 2. Configure GNSS device to output PPS (signal generated by GNSS device used for BTS synchronization) only when at least 3 satellites are visible.
Preventive / Continuous Improvements:
1, From R&D pov, there is no need to have preventive / continuous improvements, in addition to corrective action done.
2, Customer interface need to analyze from their pov, why there was unclarity in the requirements related to 24h holdover mode.
3, Related to use of Corrective Action: Feature will be proposed to be implemented in BTS that will give customer possibility to chose between
"Gnss source availability“ (GNSS can work with 1 satellite as now)" and "GNSS robustness" (anti-jamming feature turn on, 3 satellites needed).
to provide PPS). This is more like a technical product improvement.
Then performance testing on PS clock/time handling area will be part of the regular component testing and will make sure that functions will fulfill
performance requirements set to those.
Customer
Corporate Logo
Notes: 11

## Slide 12: CAS-107090-V9C1: IoT increased after activating second carrier
Description:
CAS-107090-V9C1: Second carrier's IoT is very high from the beginning of the activation of the second carrier
<Case Opened Date:.> Reported Date : 15 Mar 2018
Cause:
<Field is using an old version: The correction of CAS-49598-X4L2(Reported Date : 11 Sep 2017, tested with TL16_ENB_0000_001071_000000) , The field version is TL16_ENB_0000_001065_800002 which is not the latest version.>
< This is field version usage control issue from customer side to Nokia. Customer interface problem, not R&D issue
Escaped Defect Reason:
< This bug has been already fixed. Should be analysed in customer interface why field is still using the old version
No escape from the R&D pov
Corrective Action:
< CAS-49598-X4L2 >
<TL16_ENB_0000_001071_000000
Preventive / Continuous Improvements:
<This is not R&D issue, Need Customer Interface provide.
<No test changed from R&D side, this is not R&D issue
<What improvement(s) were implemented and being controlled; ie updated process doc, enhanced checklist,
added metric to manage compliance, etc need Customer Interface provide, Not R&D issue.
Customer
Corporate Logo
RCA/EDA is ongoing, waiting input from Lei, Enqing
Notes: 12

## Slide 13: CAS-180942-R1S2: IOT increased several times after 12 sites upgraded from TL16RE 0.5 to TL18SPRE 0.3 3 days later
Description:
<CAS-180942-R1S2: IOT(Interference over Thermal) counters are very high(abnormal) but the UL SINR is normal, IOT related KPIs are abnormal but other KPIs keeps normal>
<Case Opened Date:.> Reported Date : 07 Nov 2018
Cause:
<By incorrectly condition judgement usage cause accumulative thermal noise values will always be dropped, further cause InteferencePowerCounter abnormal>
<Injected by refactory/Optimization. Refine/Optimization process is not followed strictly>
Escaped Defect Reason:
< SCT case was missing. This error is triggered only when PUCCH and PUSCH measurement from ULPHY was not reached to MACPS at the same TTI , ET and ST is difficult to cover this issue
Corrective Action:
< CAS-180942-R1S2 >
< TL18_ENB_0000_020007_000000
Preventive / Continuous Improvements:
<Refine/Optimization process improvement, adding optimization solution assessment process, select the most security optimization solution
which has the least impact on legacy code and US to avoid leading new defect
<Add One SCT case to cover this.
<Update Optimization process and add security assessment for optimization solution in optimization checklist .>
Customer
Corporate Logo
Notes: 13

## Slide 14: Backup

## Slide 15: Customer Name: Case Abstract
Description:
<Customer Case Number: Include descriptive content from RESOLVE case.>
<Case Opened Date:.>
Cause:
<Why did it fail? Describe what was wrong in the product. Product viewpoint information.>
<Why was the problem injected? What was the process failure that led to the product failure?>
Escaped Defect Reason:
<Why did it escape the test phases?>
Corrective Action:
<Fault (Pronto) ID>
<SW/HW release info for the correction, or description of other corrective action if not corrected by HW/SW update.>
Preventive / Continuous Improvements:
<What process changes are completed or planned?>
<What test changes are completed or planned?>
<Define how we will confirm that improvement(s) were implemented and being controlled; ie updated process doc, enhanced checklist,
added metric to manage compliance, etc.>
Customer
Corporate Logo
Notes: 15